## Slide 1: Resource partitioning and latency hiding

## Slide 2: What is latency ?
number of clock cycles between instruction being issued and being completed
  Arithmetic instruction latency
  Memory operation latency

## Slide 3
Operation | Tesla GT200 | Fermi GF106 | Kepler GK104 | Maxwell GM107
ADD/SUB | 24 | 16 | 9 | 6
MAX/MIN | 24 | 18 | 9 | 12
MAD | 120 | 22 | 9 | 13
MUL | 96 | 20 | 9 | 13
Div | 608 | 286 | 141 | 210
Rem | 728 | 280 | 138 | 202
AND, OR, XOR | 24 | 16 | 9 | 6

## Slide 5: Latency hiding
The execution context of each warp processed by and SM are maintained on-chip during the entire lifetime of the warp.
Therefore switching from one execution context to another has no cost.

## Slide 6
1
2
3
20
21
W1
W1
W2
W3
W20
Execution cycle

## Slide 7
1 SM -> 128 cores
4 x 20= 80
13 * 80 = 1040
can execute 4 warps parallelly in one SM
To hide the latency of per SM
To hide the latency of per device

## Slide 8: How about memory latency
Lets consider DRAM latency of Maxwell architecture as 350 cycles .
  GTX 970 have bandwidth of 196 GB/s
  Nvidia-smi -a -q -d CLOCK
  3.6 GHz memory clock
  196 / 3.6 = 54 Bytes/cycle

## Slide 9
SM1
SM3
SM2
SM4
DRAM
54 byte/cycle

## Slide 10
54 * 350 = 18900 Bytes
18900 / 4 = 4725 threads
4725/ 32 = 148 warps
148 / 13 -> 12 warps per SM

## Slide 11: Categorizing CUDA applications
Bandwidth bound applications
Computation bound applications