## Slide 1: CUDA memory types

## Slide 2
L2
Global memory
Texture memory
Constant memory cache
Register files
SMEM
L1
Constant
Read only
Streaming multiprocessor
DRAm/
Device mem

## Slide 3: Registers
* Fastest memory space in the GPU
* Use to hold frequently accessed thread-private variables, and arrays if the indices are constant or can be determine at compile time.
* share their lifetime with the kernel

## Slide 4
On Fermi GPUs one thread can have maximum of 63 registers. But all other microarchitectures allowed to have maximum of 255 registers per thread.

## Slide 5: Register spills
If a kernel uses more registers than the hardware limit, the excess registers will spill over to local memory. This register spilling can have adverse performance consequences.

## Slide 6: Launch bounds
__launch_bounds__(maxThreadsPerBlock, minBlocksPerMultiprocessor)
Ex : __global__ void __launch_bounds__(48)
register_usage_test(int * results, int size)

## Slide 7
-maxrregcount=32

## Slide 8: Local memory
Store variables which are eligible for registers but cannot fit into the register space
  local arrays with indices which cannot resolve at compiler time.
  Large local structures
Not an on-chip memory, allocates in DRAM so have high latency memory access

## Slide 9: Shared memory
Shared memory is on chip memory which partition among thread blocks.
          __shared__
The L1 cache and shared memory for an SM use the same on-chip memory

## Slide 10
Constant memory
Texture Memory
Global Memory
GPU Caches