## Slide 1: Resource partitioning and latency hiding

## Slide 2
The local execution context of a warp mainly consists of the following resources:
        Program counters
        Registers
        Shared memory
The execution context of each warp processed by a SM is maintained on-chip during the entire lifetime of the warp. Therefore, switching from one execution context to another has no cost

## Slide 3
Registers and shared memory can be directly controlled by the programmer.
set of 32-bit registers stored in a register file that are partitioned among threads, and a fixed amount of shared memory that is partitioned among thread blocks.

## Slide 4
More warps with fewer register per thread
Fewer warps with more register per thread
Warps

## Slide 5
fewer blocks with more shared memory per block
More blocks with less shared memory per block
Thread blocks

## Slide 6
Technical spec | 3 | 3.5 | 5 | 6 | 7
Max concurrent block per SM | 16 | 16 | 32 | 32 | 32
Max concurrent warps per SM | 64 | 64 | 64 | 64 | 64
No register per SM | 64K | 64K | 64K | 64K | 64K
Max Register per thread | 63 | 255 | 255 | 255 | 255
Shared memory per SM | 48K | 48K | 64K | 64K | 96k

## Slide 7: Warp categories in SM
Active blocks/warps
  Selected warp
  Stalled warp
  Eligible warp
Resources have been allocated
actively executing
ready for execution but not currently executing
not ready for execution

## Slide 8
32 CUDA cores should free for execution
All arguments to the current instruction for that warp should ready
Conditions to be a eligible warps