## Slide 1: Shared memory

## Slide 2
Nature of the algorithm we are going to implement forces us to have miss-align, non-coalesced memory anyway.
In such cases we can improve performance of our kernels greatly by utilizing shared memory.

## Slide 3
L2
Global memory
SMEM
L1
Read only
constant
On Chip
On board

## Slide 4: Shared memory usage
An intra-block thread communication channel
A program-managed cache for global memory data
Scratch pad memory for transforming data to improve global memory access patterns

## Slide 5
Compute Capability | 2.0 | 2.1 | 3.0 | 3.2 | 3.5 | 3.7 | 5.0 | 5.2 | 5.3 | 6.0 | 6.1 | 6.2
Shared Memory / Multiprocessor (bytes) | 48K | 48K | 48K | 48K | 48K | 112k | 64K | 96K | 64K | 64K | 96K | 64K

## Slide 6
A fixed amount of shared memory is allocated to each thread block when it starts executing
This shared memory address space is shared by all threads in a thread block.
Its contents have the same lifetime as the thread block in which it was created.

## Slide 7: Optimizing memory access
1. Counting on L1 cache to store repeatedly access memory
2. Store repeatedly access memory explicitly in shared memory (using shared memory as program managed cache)

## Slide 8
Global memory
Shared mem
SM
One time access of global memory to SM