## Slide 1: Shared memory banks and access modes

## Slide 2: Shared memory bank

## Slide 3: Bank conflict
When multiple addresses in a shared memory request fall into the same memory bank, a bank conflict occurs, causing the request to be replayed.
The hardware splits a request with a bank conflict into as many separate conflict-free transactions as necessary

## Slide 4: Parallel access of memory banks
When multiple addresses accessed by a warp fall into multiple banks, ideally all 32 banks then parallel access of shared memory occurs. This pattern implies that some, if not all, of the addresses can be serviced in a single memory transaction

## Slide 5: Parallel access

## Slide 7: Sequential access
Threads access different memory address in same bank
B1 | B2 | B3 | B4 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | B30 | B31
T1 | T2 | T3 | T4 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | T30 | T31

## Slide 8: Broadcast access
Threads access same memory address in same bank
B1 | B2 | B3 | B4 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | B30 | B31
T1 | T2 | T3 | T4 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | T30 | T31

## Slide 9: Shared memory bank width
Compute capability 2.x have 32 bit banks
Compute capability 3 or later have 64 bit banks

## Slide 10: Shared memory access modes
32 bit
64 bit
fermi device have only 32 bit memory bank width, only 32 bit access mode will be applied. But for devices which have 64 bit shared memory bank width we can configure access mode to be 32 bit or 64 bit depending on the applications.

## Slide 11: 32 bit access mode
0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
B1 | B2 | B3 | B4 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | B30 | B31
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | - | - | - | - | - | - | - | - | - | - | - | 30 | 31
32 | 33 | 34 | 35 | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | - | 61 | 62 | 63
Byte Memory address
4-byte word index

## Slide 12: Simple equation to find bank index for 32 bit bank width devices
bank index = (byte address ÷ 4 bytes/bank) % 32 banks

## Slide 13: Bank width is 64 bits and access mode is 32 bit
B1 |  | B2 |  | B3 |  | B4 |  | B5 | 
B30 |  | B31 | 
0
32
1
33
2
34
3
35
4
36
30
62
31
63
successive 32 bit or 4 bytes of memory will be mapped to successive memory banks

## Slide 14: Bank width is 64 bits and access mode is 32 bit
B1 |  | B2 |  | B3 |  | B4 |  | B5 | 
B30 |  | B31 | 
0
2
3
4
5
6
7
8
9
10
60
61
62
63
Then successive 64 bit is going to mapped to successive banks

## Slide 15
B1 | B2 | B3 | B4 | B5
 | A | B |  | 
No bank conflict

## Slide 16
B1 | B2 | B3 | B4 | B5
 | A |  |  | 
No bank conflict

## Slide 17: Bank conflicts in 32 bit banks
B1 | B2 | B3 | B4 | B5
 | A |  |  | 
 | B |  |  | 
bank conflict

## Slide 18: Bank conflicts in 64 bit banks
B1 |  | B2 |  | B3 |  | B4 |  | B5 | 
 |  | A | B |  |  |  |  |  | 
No bank conflict

## Slide 19: Bank conflicts in 64 bit banks
B1 |  | B2 |  | B3 |  | B4 |  | B5 | 
 |  | A |  |  |  |  |  |  | 
 |  |  | B |  |  |  |  |  | 
2 way bank conflict

## Slide 20: Bank conflicts in 64 bit banks
B1 |  | B2 |  | B3 |  | B4 |  | B5 | 
 |  | A |  |  |  |  |  |  | 
 |  |  | B |  |  |  |  |  | 
 |  | C |  |  |  |  |  |  | 
3 way bank conflict